## Slide 1: AN EXPLORATION OF MACHINE LEARNING MODELS FOR SPATIAL-TEMPORAL METEOROLOGICAL FORECASTING
Drew Yohe
ECE 2372

## Slide 2: Background
Accurate long-term predictions of meteorological features such as temperature, precipitation have always been of public and private sector interest
Prior to the last decade, numerical physics models were best-in-class, but recently, ML approaches have started to outperform conventional models
This project explores which architectures have the most potential, and explores techniques that can be used to overcome difficulties in the process
Three architectures will be explored

## Slide 3
Outline
Predictive Model
Raw Data
Dense Spatial Feature Map
Reduced Dimension Spatial Feature Matrix
Reduced Dimension Spatial-Temporal Feature Tensor
Time
Reduced Dimension Spatial Feature Prediction
Densification Model
Expansion Model
Dense Spatial Feature Prediction
Dimensionality Reduction
Layer

## Slide 4: Data Sourcing
The database used for training and assessment is the National Oceanic and Atmospheric Administration’s (NOAA) hourly weather data from the US Climate Reference Network (USCRN)
This provides sparse data across the United States of many features, such as solar radiation, soil temperature, relative humidity, atmospheric temperature, and precipitation
Figures in this presentation will primarily focus on temperature profiles, but the approach is generalizable

## Slide 5: Densification - Approach
To develop appropriate training tensors, having data spatially uniform is critical
By dividing the complete data set into a training and testing subset, generalization of each model can be evaluated
Full Set (130 stations)
Training Set (50 stations)
Testing Set (80 stations)

## Slide 6: Densification - Models
To develop appropriate training tensors, having data spatially uniform is critical
By dividing the complete data set into a training and testing subset, generalization of each model can be evaluated
Nearest Interpolation
Linear Interpolation
Feed-Forward NN
2
128
128
256
1
Normalized coordinates
Normalized feature value
Feed-Forward NN architecture for densification
(Leaky ReLU activation between layers)

## Slide 7: Densification - Results
Overall, the feed-forward architecture yielded the lowest generalization error and has other benefits, so feature densification will be performed with this model
Model Result | Nearest Interpolation | Linear Interpolation | Feed-Forward NN
Average Error (°C) | 4.89 | 4.47 | 4.30
Feature Map Continuity | Poor | Moderate | High
Map Coverage | Full | Partial | Full
Computational Complexity | Low | Low | High

## Slide 8: Dimensionality Reduction
Increasing the resolution of the feature matrix will improve the relative loss, but with a large increase in computational complexity. Ultimately 20x56 was chosen (1120 features)
5x14
10x28
20x56
140x50

## Slide 9: Temporal Layering
Generating the spatial feature maps for 48 consecutive hourly time steps enables the creation of a layered tensor that contains normalized uniform spatial-temporal data, which is optimal for a predictive ML architecture
20x56
48 hours
48x20x56 (53,760 feature values)

## Slide 10: Predictive Models – Feed Forward
128
256
512
20x56
48 hours
48x20x56
53,760
Total Parameters: 27,834,336
1,120
Flatten
Reshape
Prediction of next hour
All activation functions are leaky ReLU

## Slide 11: Predictive Models – 3D Convolution
128
256
512
20x56
53,760
Total Parameters: 28,001,056
1,120
Reshape
Prediction of next hour
48 hours
48x20x56
Max Pool 3D
Max Pool 3D & Flatten
32 Conv3d Filters (3x3x3)
64 Conv3d Filters (3x3x3)
1 Channel
32 Channels
64 Channels
1 Channel
All activation functions are leaky ReLU

## Slide 12: Predictive Models – LSTM
128
256
512
20x56
1,120
1,120
Reshape
Prediction of next hour
All activation functions are leaky ReLU
LSTM Cell
LSTM Cell
LSTM Cell
1,120 inputs x 48 steps
1,120 outputs
48 hours
Reshape
3 Layers
48x20x56
Total Parameters: 31,125,600

## Slide 13: Predictive Models – Expansion
20x56
2
128
128
256
1
Model Output
Normalized feature value
Reuse densification network for expansion, but the training data is the reduced dimension output
Normalized coordinates
Dense Final Prediction
100x280

## Slide 14: Predictive Models - Output

## Slide 15: Predictive Models - Results
Accuracy is computed as the percentage of stations that are within 3°c of the true value
Overall, the 3D convolutional NN architecture had the best performance, however the LSTM model performed comparably and held steady, even at far-future time steps
The feed-forward network had poor early performance, dipping below 50% accuracy within 48 hours

## Slide 16: Discussion and Future Considerations
There are many architectures involved in the entire prediction process, many of which could benefit from further development
Hybridization of the best performing models could yield even better results than found here
Adding a fourth dimension to the feature tensor of additional weather values could add insight into feature interplay
Precipitation Map

## Slide 17: Referenced Literature